## Slide 1: Ambulatory aids and gait training
Dr. Osama Neyaz
Assistant Professor
Department of PMR

## Slide 2: Ambulatory Aids
Assistive devices for mobility/ambulation.
Provide support and transmit body weight.

## Slide 3: Types
Canes
Crutches
Walkers

## Slide 4: Whom to be given?
who have difficulty maintaining their center of gravity within support area.
It increases the area of support.

## Slide 5: How it works?
Improve balance
Redistribute and extend the weight-bearing area
Reduce lower limb pain
Provide small propulsive forces
Provide sensory feedback.
They should be considered an extension of the upper limb.

## Slide 6: Pre-requisite for use
Adequate upper limb strength and coordination
Endurance
Stability
An exercise program for the upper limbs and a supervised period of training program is recommended.

## Slide 7: Which type of aid needed ?
Depends on how much balance and weight-bearing assistance is required.
The body weight transmission -
Unilateral cane - 20% to 25%
Forearm or Arm cane - 40% to 50%
Bilateral crutches - up to 80%.

## Slide 8: Canes
Length Measurement –
Tip of the cane at the level of the greater trochanter in an upright position.
Elbow flexed approximately 20 degrees
Cane with height adjustable notches - “one cane fits all”

## Slide 9: Canes
Parts - handle, shaft, and base
Material – woods, metal especially aluminum, plastics, and carbon fibre.
Types - C cane (crook top cane or J cane), Functional grip Cane, Quad cane

## Slide 10: Canes
The cane usually is held on the side opposite the affected leg.
The patient advances the cane and the affected foot, then moves the unaffected foot.

## Slide 11: Crutches
Types -
Underarm (Axillary)
Forearm (Lofstrand)
Canadian (Triceps crutch)
Forearm support (Platform crutch)

## Slide 12: Axillary crutch
Length: anterior axillary fold to a point 6 inches lateral to the fifth toe with the shoulders relaxed.
Crutch handle : elbow flexed 30 degrees, the wrist in maximal extension, and the fingers forming a fist, crutch 3 inches lateral to the foot.

## Slide 13: Forearm (Lofstrand)
Length: standing upright with elbow in 20 degrees of flexion.
Less supportive than axillary crutches for ambulation.

## Slide 14: Platform Forearm Crutch
Length: The distance from the ground to the forearm rest with the shoulders relaxed and the elbows flexed 90 degrees
Indications - painful wrist & hand conditions, elbow contractures.

## Slide 15: Commonly used crutches and canes

## Slide 16: Walker
Length: patient stand upright and the elbows flexed 20 degrees. Front of the walker 12 inches in front of the patient.
Provides maximum support but a slow gait.
Front wheels facilitate movement of the walker for those who lack upper limb coordination.
Useful for hemiplegia and ataxia.

## Slide 17: Walker types
Standard walker
Wheel walker
Reverse walker
Platform walker

## Slide 18: Gait Patterns
Foot sequence of an individual using assistive devices.
Gait pattern depends upon ability to-
Move the feet reciprocally
Tolerate full load on each leg
Lift the body off the floor
Maintain the balance

## Slide 19: Gait Patterns
Alternating (reciprocal) gait pattern
    Four-point gait
    Two-point gait
    Three-point gait
Swinging (simultaneous) gait pattern
    Swing-to gait
    Swing-through gait

## Slide 20: Four-point Gait

## Slide 21: Three-point Gait

## Slide 22: Two-point Gait

## Slide 23: Swinging (Simultaneous) Gait Pattern
    Swing-to gait
    Swing-through gait

## Slide 24: Amputation - Gait training

## Slide 25: Amputation - Gait Training
Steps:
Weight-bearing and balance training
Basic Gait training
Advance gait training
Functional training

## Slide 26: Weight Bearing and Balance
Partial weight bearing (with & without support)
Partial weight shift (with & without support)
Pelvic rotation training
Sideward walking (two-hand support)
Full weight shift (with & without support)
Heel strike (with or without support)
Handball (with or without support)

## Slide 27: Partial Weight Bearing

## Slide 28: Partial Weight Shift

## Slide 29: Pelvic Rotation Training & Sideward Walking

## Slide 30: Full Weight Shift

## Slide 31: Heel Strike

## Slide 32: Handball

## Slide 33: Basic Gait Training
Sound-leg step forward & backward (two-hand support)
Sound-leg step through (with & without support)
Prosthetic-leg step forward & backward (two-hand support)
Prosthetic-leg step through (two-hand support)
Prosthetic-leg step forward (one-hand support)
Prosthetic-leg step through (without support)
Walking between the parallel bars (with & without support)

## Slide 34: Sound-leg Steps

## Slide 35: Sound-leg step through
Sound-leg step through

## Slide 36: Walking between the parallel bars

## Slide 37: Thank You